## Slide 1
Data Mining Medical Device Repair Logs
FBlock

## Slide 2: Problem statement
FDA currently has two primary adverse event reporting systems: MedSun and MedWatch
These systems receive adverse event reports on medical devices from the US and abroad
Reports from the clinical community must be proactively sent to FDA (time intensive) – around 45 minutes by a trained reporter
What if there was a less time burdensome approach for FDA to receive real-world clinical evidence on medical devices?
This system would be used by analysts at FDA to facilitate discussions with clinicians on medical device problems or can be used to initiate or support a medical device safety device signal

## Slide 3: Dataset
FDA’s MedSun program has initiated a pilot project to collect medical device repair logs from a subset of its facilities
Logs are received on a quarterly basis, and they are not time intensive to upload. They cover repairs on infusion pumps, ventilators, anesthesia systems, and defibrillators
This source of real-world device data likely contains potential device safety signals which may otherwise have been unnoticed and unreported
Amassed over 215K repair logs since as early as 2015
Type | Model | Requested | Failure Reason | Reason | Labor Report
ANESTHESIA MACHINE - AESTIVA | AESTIVA/5 7900 | 1/16/2018 | Hardware Failure | Aestiva O2 cell wont calibrate | Found the O2 sensor cable damaged. Replaced cable and calibrated
ANESTHESIA MACHINE - AESTIVA | AESTIVA/5 MRI | 3/12/2018 | Hardware Failure | Anesthesia Unit, Aestiva MRI ABS leaks | Reseated CO2 canister and verified proper operation.

## Slide 4: Variables of interest
Main variable of interest: free text narrative repair descriptions
  Work Order problem description / Work Order repair description
  Any additional information about the device / repair
Device identifiers – we need to know specifically what device has the problem
  Manufacturer name
  Brand of device
  Model number
Previous recalls or potential safety signals – these can serve as guides or be used to better train the model

## Slide 5: Supervised Approach
As we actively receive reports from our collaborates, we are reviewing the logs and flagging any log which represent a potential safety signal
This training set will then be fed into our model to enhance the detection of future potential safety signals
Our target variable is a log or set of logs that describe potential safety signals

## Slide 6: Challenges
From our analysis, there is a lot of noise in our data and very few potential signals (routine maintenance)
Are there any current potential safety signals in our logs?
Significant tradeoffs in any developed model:
  Over-training will give us fewer logs but, only tell us what we already know
  A wider net will provide too many logs to review (all of them?)
  We need the model to find previously undetected potential safety signals

## Slide 7: Plan of Action
Expand and enhance our current XGBoost model through additional testing and training with current datasets
Explore additional modeling techniques to ensure the capture of the potential safety signals
 | Objectives | Jul |  |  |  | Aug |  |  |  | 
1 | Evaluate current data as received |  |  |  |  |  |  |  |  | 
1.1 | - Optimize XGBoost model |  |  |  |  |  |  |  |  | 
1.2 | - Trained model with Q2 2018 logs |  |  |  |  |  |  |  |  | 
2 | Evaluate alternative techniques |  |  |  |  |  |  |  |  | 
2.1 | - Never-Ending Language Learning |  |  |  |  |  |  |  |  | 
2.2 | - K-means / K-medoids clustering |  |  |  |  |  |  |  |  | 
2.3 | - MxNet |  |  |  |  |  |  |  |  | 
2.4 | - Other techniques |  |  |  |  |  |  |  |  |